## Slide 1
OmniSee
SCALABILITY AND POC READINESS
OmniSee at 80,000 cameras
Compute, accelerators, bandwidth, storage, operations, resilience, security and cost: one response to the scalability criterion.
Sizing basis: the repository’s own capacity measurements plus stated assumptions. Costs are budgetary, in ₹, ±30%.
80,000 tiles, one wall: edge analytics, regional hubs, one control plane
Notes: Opening. This deck answers the seven scalability questions for the 80,000-camera target. Every number is tagged MEASURED (from scripts/capacity), MODELLED (derived from those measurements plus stated assumptions) or PLANNED (design not yet built). The assumption register is the last slide.

## Slide 2: 80,000 cameras fit if the video stays at the edge
00 · SUMMARY
1 + 8 + 160
Central site (+ DR), regional hubs, edge nodes of about 500 cameras each
DESIGN
4.5 Mbps
of results reach the centre, instead of 160 Gbps of raw video
MODELLED
~50 GPUs
40 × L4 for plates and detectors, 10 × L40S for scene reasoning
MODELLED
17.4 PB raw
15 days at 1 Mbps: 2 days hot, 5 warm, 8 cold, erasure-coded
MODELLED
5 min / 1 h
RPO and RTO for events, alerts and control plane; evidence RPO near zero
TARGET
₹79 cr
CapEx, then ₹24 cr a year; about ₹410 per camera per month over 5 years
MODELLED
How to read the tags. MEASURED: run on the repo’s capacity suite. MODELLED: derived from it plus stated assumptions. PLANNED: designed, not yet built. Assumptions are listed on the last slide.
Notes: The central claim: do not haul video to one place. Analyse and record next to the cameras, send results. 500 cameras are 800 Mbps of video but 28 kbps of results (docs/capacity.md, docs/regional-gateway.md). All other numbers follow from that design choice.

## Slide 3: Three tiers: analyse at the edge, decide at the centre
00 · REFERENCE DESIGN
Central
State data centre + DR site
x 1 + 1
Control plane: API, scheduler, alert engine
Postgres / Timescale, 3-node HA
Event bus (Redis Streams, Kafka)
Auth, RBAC, audit, dashboards
Regional hub
~10,000 cameras each
x 8
GPU pool: ANPR and detectors
Cold tier: Ceph, S3 API
Bus mirror, DB read replica
Operator video relay
Edge node
~500 cameras each
x 160
gateway: capture, gate, analyzers
MediaMTX: WebRTC / HLS relay
Recorder: hot + warm tiers
Outbox on disk, signed uplink
Cameras and department systems: RTSP, ONVIF, Hikvision, Dahua, grid, VMS connectors
Results, alerts, evidence thumbnails: ~4.5 Mbps total, HMAC-signed, store-and-forward
Frames to GPU pool, results, clips on demand: ~3 Mbps steady per edge
Raw video stays in the district: 160 Gbps in total, never on the backbone
Notes: This is the Profile 1 shape from docs/federation-plan.md. The edge node is gateway.ts plus MediaMTX, which exist today. The regional hub tier (GPU pool, cold storage, bus mirror) is the design extension; the app does not yet route through hubs. The centre is server.ts with Postgres, Redis/Kafka.

## Slide 4: Compute by tier: central, regional and edge requirements
01 · COMPUTE
Central
1 primary site + 1 DR site
API / UI: 6 × 16 vCPU, 64 GB, stateless behind a load balancer
Scheduler 1 + standby; 8 workers for any camera without an edge node
Postgres / Timescale: 3 nodes, 64 vCPU, 512 GB, 40 TB NVMe
Bus: 5 Redis / Kafka brokers; 4 observability nodes
Regional hub
8 hubs · ~10,000 cameras each
6 servers, 32 vCPU, 128 GB: bus mirror, DB replica, S3 gateway, video relay
2 GPU hosts with 2 to 3 × L4 each
Ceph cold-tier nodes: ~0.86 PB logical per hub
25 GbE inside the hub, 1 Gbps uplink to the centre
Edge node
160 nodes + 16 spares · ~500 cameras
16 vCPU, 64 GB, 10 GbE; runs gateway, MediaMTX and the recorder
Writes ~62 MB/s sustained at 1 Mbps per camera (125 MB/s at 2 Mbps)
Disk: 10.8 TB hot and 27 TB warm per node
Needs ~3 modern cores; 16 vCPU leaves headroom for re-encode and peaks
Basis. Platform code costs 0.54 ms per analysed frame, flat from 500 to 80,000 cameras (measured). Hardware is provisioned at about 4× the modelled need because every measurement came from one shared Celeron laptop.
Notes: Edge sizing: 500 cameras need about 2.8 Celeron-cores for capture, gate and platform code at 60 s (docs/capacity.md section 4) plus 3 to 5.5 Celeron-cores of MediaMTX pass-through (about 0.6 to 1.1 percent of a core and 1 MB per camera). That is about 3 modern cores if a server core is 3x a Celeron core (an assumption). 16 vCPU leaves room for H.265 re-encode slots and peaks. Re-encoding capacity itself was not measured. Central: the scheduler measured 48 ms average per tick at 80,000 cameras and about 1.4 GB process memory.

## Slide 5: The platform’s own code is not the limit at 80,000 cameras
01 · COMPUTE
Scheduler tick, average milliseconds, by fleet size
Chart: cameras
| 500 | 5,000 | 20,000 | 80,000
ms per tick | 0.6 | 1.2 | 3.8 | 48
0.54 ms
CPU per analysed frame, flat across the whole range
MEASURED
0 late runs
in 150,194 analyses at 80,000 cameras
MEASURED
1.4 GB
process memory at 80,000 cameras; budget 2 GB
MEASURED
0.125 s
CPU per RTSP still grab; start-up dominates, the largest saving available
MEASURED
Limit of the evidence. One shared Celeron N4020 laptop, with Gemini and the camera frame faked. The on-site PoC re-runs this on target servers.
Notes: Source: scripts/capacity/controlPlane.ts running the real analysis worker, analyzer pipeline, event derivation and alert engine, with the camera frame and the model answer faked. Hardware: Celeron N4020, 2 cores at 1.1 GHz, shared with a browser. Capture cost: ffmpeg start-up dominates (0.125 s CPU per still grab versus 0.016 s of ffmpeg accounting).

## Slide 6: About 50 GPUs cover plates, detectors and scene reasoning
02 · ACCELERATORS
A Plate reading (ANPR)
YOLOv9-t detector + CCT-s OCR on ONNX CUDA
333 analyses/s × 40% with vehicles = ~130 reads/s
Peak × 3 = ~400 reads/s
Assume 100 reads/s per L4
16 × L4
2 per hub, so one can fail
SERVICE BUILT
B Real-time detectors
Person, vehicle, intrusion on priority cameras
5% of cameras = 4,000 at 2 fps = 8,000 fps
Assume 500 fps per L4 for a small detector
+20% headroom
20 × L4
2 to 3 per hub, 4 cold spares
PLANNED
C Scene reasoning (VLM)
Self-hosted vision-language model, or a hosted API
Funnel leaves ~67 calls/s (see next slide)
Assume 8 requests/s per L40S
+1 spare
10 × L40S
Central, behind one endpoint
ENDPOINT BUILT
Unmeasured. No GPU has run this stack yet. Throughput per card is the first number the PoC measures. A hosted model API removes Pool C (see cost).
Notes: Pool A: the ANPR service (anpr-service/) runs a YOLOv9-t plate detector and a CCT-s OCR model through ONNX Runtime, CPU or CUDA; ANPR_DEVICE=cuda refuses to start without a working GPU. Throughput per card is an assumption, not a measurement; scripts/check-anpr.mjs measures it on real hardware and every response carries elapsed_ms. Pool B is new work: a local detector behind the existing analyzer contract. Pool C: AI_PROVIDER=openai with OPENAI_BASE_URL supports a self-hosted vLLM endpoint.

## Slide 7: A three-stage funnel keeps the model load small
02 · ACCELERATORS
1,333 /s
All cameras, one frame per 60 s
Capture at the edge, nothing leaves the region yet
333 /s
Frame gate: scene changed
25% pass (assumed); heartbeat every 10 min
67 /s
Local detector and ANPR flag it
20% of gated frames (assumed) need scene reasoning
33 /s
Notable events with evidence
10% of results; thumbnails go to the centre
Levers that move the GPU count
Interval 60 s to 300 s: five times fewer frames
Gate threshold per camera type
ANPR only on cameras that see vehicles
Hosted model API instead of Pool C
Mode per camera: AI off runs the local detector only, no model call
Fail-safe. If the ANPR service is down, the scene model reads plates and marks them gemini-fallback, so reads are never mistaken for dedicated OCR.
Notes: Numbers: 80,000 cameras at one frame per 60 s is 1,333 captures per second. The frame gate (server/frameGate.ts, 2 percent pixel change, 10-minute heartbeat) is assumed to pass 25 percent; that pass rate is the most valuable number to measure on real scenes. The local no-AI detector (server/analytics/localDetector.ts) and ANPR act as the second stage; the 20 percent pass is an assumption. Notable share of 10 percent is also an assumption from docs/capacity.md.

## Slide 8: Bandwidth: the backbone carries results, not video
03 · NETWORK
Cameras to edge
160 Gbps
1 Gbps per node at 2 Mbps; stays inside the district network
Edge to hub
3 Mbps
steady per edge: frames for the GPU pool, results, thumbnails. Provision 100 Mbps for live tiles and clip pulls
Hub to centre
20 Mbps
all hubs together: 4.5 Mbps of results + ~16 Mbps thumbnails. Provision 1 Gbps per hub
Centre to DR
9 Mbps
average database replication (~100 GB a day with indexes). Provision 1 Gbps
28,000×
less than hauling video: 500 cameras are 800 Mbps of video but 28 kbps of results
MEASURED
Live viewing is pulled on demand
An operator wall of 16 sub-stream tiles at 0.5 Mbps is ~8 Mbps. 100 walls at once is ~0.8 Gbps, served from the edge nearest each camera. The media server pulls each camera once however many people watch.
Notes: Camera to edge: 500 x 2 Mbps = 1 Gbps per node, 160 Gbps in total (at 1 Mbps, half). Edge to hub: JPEG frames for the GPU pool (about 2.08 analyses/s per 500 cameras x ~150 KB = 2.5 Mbps) plus results (28 kbps, measured) plus evidence thumbnails (about 0.1 Mbps). Hub to centre: 333 analyses/s x ~1.7 KB = 4.5 Mbps results, plus about 16 Mbps of thumbnails. DR replication: ~100 GB/day of rows including indexes (index factor assumed 2) = 9 Mbps average. The 28,000x figure: 800 Mbps of video versus 28 kbps of results for 500 cameras (docs/regional-gateway.md).

## Slide 9: Eight low-bandwidth strategies, most already in the code
03 · NETWORK
Analyse at the edge
Only results cross the link: about 28 kbps for 500 cameras.
BUILT
Frame gate
Skip a frame if under 2% of pixels moved; heartbeat every 10 minutes.
BUILT
Store and forward
Disk outbox, batches of 200, back-off from 1 s to 60 s, survives days offline.
BUILT
Pull only when watched
One pull per camera; the relay serves every viewer from that one stream.
BUILT
Link-aware playback
Plain fMP4 HLS on weak links; low-latency HLS stalled at 300 ms delay in testing.
BUILT
Sub-streams
Walls and recording on 1 Mbps sub-streams instead of 2 to 4 Mbps main streams.
CONFIG
No-AI local detector
Motion, zone and line events from a 64×36 fingerprint: no model call, no key.
BUILT
Longer intervals
300 s intervals cut frames five times; notable-only mirroring cuts writes tenfold.
BUILT
Notes: Sources: docs/regional-gateway.md (outbox, back-off, batching), docs/scale-out.md (frame gate, notable mode), docs/media-server.md (on-demand pull, HLS fmp4 versus low-latency HLS that stalled at 300 ms delay, H.265 handling), server/analytics/localDetector.ts (no-AI detector), docs/recording.md (sub-stream recording).

## Slide 10: Hot, warm and cold tiers for a 15-day retention baseline
04 · STORAGE
80,000
cameras recorded
1 Mbps
sub-stream, 10.8 GB per day each
864 TB
written per day
15 days
baseline; per-camera keepDays
Hot · day 0 to 2
Warm · day 3 to 7
Cold · day 8 to 15
Hot
Edge node, local RAID-6 disks with NVMe cache
1.73 PB logical, 2.16 PB raw
10.8 TB per edge node
Live tail and instant playback
MODELLED
Warm
Edge node, warm folder, erasure coded 6+2
4.32 PB logical, 5.76 PB raw
27 TB per edge node
Playback and clips, slower first byte
MODELLED
Cold
Regional hub Ceph, S3 API, erasure coded 8+3
6.91 PB logical, 9.50 PB raw
0.86 PB logical per hub
Clips cut from a 2 GB cache after download
MODELLED
Notes: Bitrate arithmetic: B Mbit/s uses B x 10.8 GB per day per camera. 80,000 cameras at 1 Mbps is 864 TB per day. Hot 2 days = 1.73 PB logical; warm days 3 to 7 = 4.32 PB; cold days 8 to 15 = 6.91 PB. Overheads assumed: RAID-6 1.25x, erasure coding 6+2 = 1.33x, 8+3 = 1.375x, giving 2.16 + 5.76 + 9.50 = 17.4 PB raw. The tier mechanics (hot to warm to cold to delete, holds blocking every step) are built in server/recording; tested with synthetic video and a signature-checking fake S3, not a real Ceph. Departments differ: 7 to 15+ days, some cloud, some local, which is why the baseline is per-camera policy (keepDays).

## Slide 11: Retention and bitrate move storage by about 17 times
04 · STORAGE
Raw storage by tier, petabytes
Chart: 
| 7 d, 1 Mbps: 7.9 PB | 15 d, 1 Mbps: 17.4 PB | 30 d, 1 Mbps: 35.2 PB | 15 d, 2 Mbps: 34.8 PB
Hot | 2.16 | 2.16 | 2.16 | 4.32
Warm | 5.76 | 5.76 | 5.76 | 11.52
Cold | 0 | 9.5 | 27.3 | 19
Events and logs
86 M events a day, ~48 GB of rows (~100 GB with indexes). 30 days hot in Postgres / Timescale, then compressed for a year.
MODELLED
Departments keep video
In the federated profile, departments hold footage for 7 to 15+ days. The platform keeps metadata and says "video no longer held" when it is gone.
PLANNED
Evidence
An exported clip is hashed, gets a hold, and is copied to the DR site, so it outlives routine retention.
HOLD BUILT
Notes: Raw petabytes by tier. 7 days: 2 hot + 5 warm, no cold. 30 days: 23 cold days = 19.87 PB logical x 1.375 = 27.3 PB raw. 2 Mbps doubles every tier. Logical range from docs/federation-plan.md: 6.0 PB (80,000 cameras, 1 Mbps, 7 days) to 103.7 PB (4 Mbps, 30 days). Event store: 86.4 M events per day at 80,000 cameras, 48.4 GB per day of row data (docs/capacity.md); index overhead of 2x is an assumption.

## Slide 12: Load balancing and horizontal scaling: every layer scales out
05 · OPERATIONS
Operators and dashboards
Load balancer: NGINX / Kong or Kubernetes ingress, TLS
API and UI pods × N, stateless
Scheduler (1 + standby) → queue → workers × N
Edge nodes × 160: each runs its own scheduler
Signed ingest /api/gateway/* into the event store
LAYER | HOW IT SCALES | STATUS
API / UI | Add pods; stateless | PLANNED
Analysis workers | Add workers; one job per camera id | BUILT
Scheduler | One is enough: 48 ms per tick at 80,000 | MEASURED
Edge | One node per ~500 cameras, sharded by gatewayId | BUILT
Event store | Batched writes ~900 rows/s per connection; partition by time | MEASURED
Video relay | One pull per camera; ~1% of a core per viewer | MEASURED
GPU pools | Stateless HTTP behind the balancer; /healthz | BUILT
Notes: Scheduler/worker split: ANALYSIS_ROLE=scheduler|worker over Redis/BullMQ (server/bullBackend.ts); a job per camera id; capacity = workers x ANALYSIS_CONCURRENCY. Tested only through the in-memory backend and fakes; never run against a real Redis. Kubernetes manifests with autoscaling are gap A23 (not built). Postgres write rate measured on Neon from a laptop: about 900 rows/s with batches of 100, one event at a time about 9 per second; the worker should group several frames per write.

## Slide 13: Monitoring, logging and health checks
05 · OPERATIONS
LAYER | SIGNALS THE PLATFORM ALREADY EMITS
Cameras | camera.offline / camera.online from run history; blocked, dark and over-exposed picture events
Analysis | GET /api/analysis/status: backend, queue depth, skipped-unchanged count, ANPR health and device
Edge nodes | Signed heartbeat; online, degraded or offline after 90 s; gateway.* events feed alert rules
Video relay | Media server log parsed into events; log tail endpoint for operators
GPU service | GET /healthz reports status and cuda or cpu; every reply carries elapsed_ms
Audit | Access log of refusals and sensitive actions, saved in batches to the database
Central stack to add
Prometheus, Alertmanager, Grafana
Central logs: Loki or ELK, structured JSON
OpenTelemetry traces across edge, hub, centre
One synthetic probe per hub
PLANNED
Golden signals per region
Analyses per second and late runs
Outbox depth and heartbeat age
Disk free and recorder gaps
GPU utilisation and reads per second
Notes: Existing signals: camera.offline and camera.online derived from run history; camera.blocked, camera.dark, camera.overexposed from the tamper analyzer; GET /api/analysis/status; gateway heartbeat with online, degraded, offline after 90 s and gateway.* events; the MediaMTX log parser (server/mediaEvents.ts); ANPR GET /healthz; the access log (last 2,000 in memory, batched to Firestore, 5,000-entry queue). Known gap: disk-full is not alerted (GET /api/recordings/usage exists, wiring it to an alert is a small follow-up).

## Slide 14: High availability, backup and disaster recovery
06 · RESILIENCE
RPO ≤ 5 min
events, alerts, config
RTO ≤ 1 h
control plane at the DR site
RPO ≈ 0
held evidence (replicated)
COMPONENT | HIGH AVAILABILITY | BACKUP | DISASTER RECOVERY
Event database | 1 primary + 2 replicas, automatic failover | WAL archive to object store; daily base copy | Async replica at DR site
Bus and queue | 3 to 5 brokers, replication 3 | Topic replay window of 7 days | Mirrored to DR
Control plane | ≥3 pods across racks; standby scheduler | Stateless; config in Git | Warm standby, DNS cut-over
Edge node | 1 spare per 10; cameras re-pointed by gatewayId; outbox holds 7 days | Camera list re-fetched from the centre | Keeps analysing offline, replays in order
Video storage | RAID-6 hot; erasure coding 6+2 warm, 8+3 cold | Not backed up (routine footage) | Region loss costs routine footage; evidence survives
DESIGN: A22 / A23 NOT BUILT
Built today: edge outbox with replay, idempotent event ids, evidence holds. Quarterly failover drills are part of the plan.
Notes: RPO and RTO are proposals for the State to confirm, not measurements. What is built: edge outbox and replay (24 gateway tests over real HTTP including a 20,000-item backlog, link cut and restore with nothing lost or doubled), idempotent event ids, evidence holds. Honest gaps: a dead gateway is not taken over by anyone (shown as gateway.offline); the centre keeps its applied-id list in memory so a confirmation lost just before a restart can apply twice; Redis and Kafka were never run; Kubernetes and DR are design only (gaps A22, A23).

## Slide 15: Cybersecurity: what is built, and what the State deployment adds
06 · SECURITY
DOMAIN
BUILT INTO THE PLATFORM
ADDED FOR THE STATE DEPLOYMENT
Identity
Sign-in, role claims (viewer, operator, admin), department scoping, access log of refusals and sensitive actions
SSO and multi-factor, privileged-access workflow, revoked-token checks on
Edge trust
HMAC-SHA256 signed requests with time and nonce; secrets rotate or disable; a stolen secret reaches only its own cameras
mutual TLS, certificate rotation, signed software updates for edge nodes
Data
SHA-256 evidence manifests, holds, camera credentials sealed, keys held server-side only
AES-256 at rest, TLS 1.3 everywhere, KMS or HSM, signed manifests
Network
Edge reaches out; the GPU service is exposed through an outbound tunnel, no inbound port
Camera VLANs, edge DMZ, per-department segments, WAF and rate limits
Operations
Alert rules on gateway and camera health events
SIEM feed, vulnerability scans, penetration test, independent audit, immutable backups
Notes: Built: Firebase Auth with role custom claims (viewer, operator, admin) and department scoping (docs/authz.md); access log; HMAC-SHA256 gateway signing over method, path, body hash, time and nonce with 5-minute skew and replay refusal (docs/regional-gateway.md); per-gateway secret rotate and disable; SHA-256 evidence manifests and holds (docs/recording.md); API keys server-side only; ANPR shared key. Not built (gap A21): encryption at rest, mTLS, network segmentation, KMS, signed manifests, SIEM export, gateway software updates. Compliance alignment is a plan item, not a claim.

## Slide 16: Implementation cost: about ₹79 crore one-time
07 · COST
One-time cost, ₹ crore
Chart: 
| Engineering, 24 months | Storage, 3 tiers | Edge servers (176) | Camera onboarding | Contingency 10% | Regional hubs (8) | GPUs and hosts | Central site | Edge network | DR site | Security and audit | Training
crore | 18 | 14.9 | 10.6 | 8 | 7.2 | 5.8 | 3.6 | 3.6 | 2.4 | 2.2 | 1.5 | 1
₹78.8 cr
Hardware 43.1, implementation 28.5, contingency 7.2
Unit prices assumed
Raw storage ₹8,000 to 10,000 per TB, complete
Edge server ₹6 lakh
L4 ₹2.8 lakh; L40S ₹9 lakh
Engineer ₹2.5 lakh per month
Onboarding ₹1,000 per camera
MODELLED ±30%
Notes: Budgetary, +/-30 percent, for the 15-day, 1 Mbps baseline. Unit prices (assumed): storage per raw TB hot 10,000 / warm 8,000 / cold 8,500 rupees including servers, network and 5-year support; edge server 6 lakh; L4 2.8 lakh; L40S 9 lakh. Storage: 2,160 TB x 10k + 5,760 TB x 8k + 9,500 TB x 8.5k = 14.9 crore. Edge: 176 servers x 6 lakh = 10.6 crore + 2.4 crore network. Engineering: 30 people x 24 months x 2.5 lakh = 18 crore. Onboarding: 80,000 cameras x 1,000 rupees = 8 crore. Contingency 10 percent. Hardware 43.1, implementation 28.5, contingency 7.2, total 78.8.

## Slide 17: Operating cost: about ₹24 crore a year, ₹410 per camera per month
07 · COST
Cumulative cost, ₹ crore
Chart: 
| Y0 | Y1 | Y2 | Y3 | Y4 | Y5
cumulative | 78.8 | 99.8 | 124.2 | 148.6 | 173 | 197.4
ANNUAL RUN COST | ₹ CR
Operations team (SOC, SRE, support, 8 developers) | 7.8
Network links (may use the State network) | 6.2
Power and cooling (~450 kW IT load) | 5.0
Hardware support, from year 2 | 3.4
Software support and audits | 2.0
Total, steady state | 24.4
What moves the number
30-day retention: +₹15 cr storage
2 Mbps recording: +₹15 cr
Hosted model API: −₹1.4 cr now, +₹6 cr a year
Notes: Annual: power 5.0 (about 450 kW IT load x PUE 1.6 x 8,760 h x 8 rupees per kWh), hardware support 3.4 (8 percent of 43.1, from year 2), operations 7.8 (18 + 8 people x 2.5 lakh x 12), network 6.2 (160 x 25,000 per month x 12 + 8 x 1.5 lakh x 12; may ride the existing State network), software support 1.5, audits 0.5 = 24.4. Year 1 has warranty so 21.0. Cumulative: 78.8, 99.8, 124.2, 148.6, 173.0, 197.4 crore. Per camera per month: 197.4 crore / (80,000 x 60) = about 411 rupees. Sensitivities: 30-day retention adds 15.1 crore of storage; 2 Mbps at 15 days adds 14.9; a hosted model API instead of 10 L40S saves about 1.4 crore up front but costs about 6.3 crore a year at an assumed 0.03 rupees per call (5.76 M calls a day), so self-hosting wins at this volume (benchmark with npm run ai:bench).

## Slide 18: What is verified, and what the PoC must still prove
08 · EVIDENCE
Verified so far
Control plane simulated to 80,000 cameras: 150,194 analyses, no late runs
Edge protocol: 24 tests over real HTTP, 20,000-item backlog, link cut and restored, nothing lost or doubled
Cold tier against a signature-checking S3: lost uploads, 40 MB streamed upload, clips with identical hashes
Real media server: pass-through about 1% of a core per camera
Event stores on real Postgres: ~900 rows/s batched, answers match the in-memory store
Not yet verified
Redis queue, Kafka, Ceph, Kubernetes: written against fakes or not written
Any GPU: ANPR speed and accuracy on CUDA, on Indian plates
Real cameras, H.265, links of hundreds of kilometres
Model latency and cost, and the real frame-gate pass rate on real scenes
Regional hub tier, edge clip fetch, gateway failover, encryption at rest, DR drills
Notes: This slide exists so the scalability claims are not read as more than they are. Sources: docs/capacity.md section 6 (not measured), docs/regional-gateway.md (not built or verified), docs/recording.md, docs/federation-plan.md gap stack.

## Slide 19: From on-site PoC to 80,000 cameras in three gated phases
08 · POC AND ROLLOUT
PoC
3 months · 100 to 500 cameras
1 edge node, 1 GPU
Own feed + Government feed
ANPR, intrusion, objects, reports
Gate: measured reads/s and gate pass rate
Pilot
6 months · 10,000 cameras
1 regional hub, 10 to 20 edge nodes
Real Redis, Kafka, Ceph
Failover and DR drill
Gate: SLOs met, cost per camera confirmed
Rollout
12 months · 80,000 cameras
8 hubs in waves
DR site live, audit passed
Hand-over to operations
Gate: sign-off per wave
WHAT THE POC MEASURES
01
Frame-gate pass rate on real scenes
02
ANPR reads/s and accuracy per L4
03
Cameras per core with in-process capture
04
Real bitrate per camera and link
05
Kill an edge node, the database primary, a link
Notes: Phase sizes are proposals. Each gate is a measurement, so the cost and GPU figures in this deck are corrected by data before the next tranche is committed. The PoC runs on the participant feed and the Government-provided feed.

## Slide 20: Assumption register: change one, and the numbers follow
APPENDIX · ASSUMPTIONS
# | ASSUMPTION | VALUE | SOURCE | IF WRONG
1 | Fleet and sampling | 80,000 cameras, 1 frame per 60 s | Brief; capacity model | Scales captures linearly
2 | Frame-gate pass rate | 25% | Assumed | Model calls and GPUs scale with it
3 | Second-stage pass rate | 20% of gated frames | Assumed | Pool C size
4 | Server core versus Celeron N4020 core | 3× | Assumed | Edge and central CPU
5 | Vehicle share of analysed frames | 40% | Assumed | Pool A size
6 | GPU throughput | 100 reads/s and 500 fps per L4; 8 req/s per L40S | Assumed | GPU count; measured in PoC
7 | Recorded bitrate and retention | 1 Mbps, 15 days, hot 2 / warm 5 | Planning default | Storage, up to ~17×
8 | Storage overhead | RAID-6 1.25×, EC 6+2 1.33×, EC 8+3 1.375× | Typical | Raw petabytes
9 | Event index overhead | 2× row data | Assumed | Database size
10 | Prices and staffing | See cost slides | Budgetary | ±30% on cost
Notes: These are the inputs behind every MODELLED tag. The sizing formulas live in scripts/capacity/model.ts and the tables are reproduced by scripts/capacity/report.ts.