## Slide 1
OmniSee
SOLUTION, ARCHITECTURE AND SCALABILITY
OmniSee at 80,000 cameras
Problem and model, architecture, interoperability, video analytics output, and the design and cost of scaling to 80,000 cameras.
Sizing basis: the repository’s own capacity measurements plus stated assumptions. Costs are budgetary, in ₹, ±30%.
80,000 tiles, one wall: edge analytics, regional hubs, one control plane
Notes: SPEAKER NOTES Open with the one-line promise: this is a platform that turns tens of thousands of department cameras into one searchable picture, and this deck shows both what it does and how it scales to about 80,000 cameras. Say that every number is tagged as measured, modelled or planned, so the audience always knows how firm it is. If asked: Why tags? Because we measured on one laptop and will not present a model as a measurement. SOURCES AND DETAIL Opening. This deck answers the seven scalability questions for the 80,000-camera target. Every number is tagged MEASURED (from scripts/capacity), MODELLED (derived from those measurements plus stated assumptions) or PLANNED (design not yet built). The assumption register is the last slide.

## Slide 2: Many owners, 80,000 cameras, and one picture is needed
SOLUTION · PROBLEM AND MODEL
Fragmented ownership
Every department runs its own system. Retention is 7 to 15+ days; some use cloud, some local storage.
Too much to watch
80,000 cameras cannot be watched by people, or hauled to one place: about 160 Gbps of video.
Incidents cross borders
A vehicle or person moves between districts and departments; evidence is scattered and expires.
Nothing may break
Department systems must stay unaffected: read-only access, and no new layer where one is forbidden.
PROPOSED MODEL: ONE PLATFORM, THREE DEPLOYMENT PROFILES
Unified viewing
Direct to each camera or system, no intermediate layer. Walls, plate metadata, tagging, searchable movement, alerts.
Federation middleware
Connectors and an event bus give departments one interface. Cross-system correlation; video stays with its owner.
Central VMS, regional edge
Statewide recording in hot, warm and cold tiers, ANPR and tracking across locations, about 80,000 cameras.
Why one platform. Connectors, events, analyzers, rules and search are shared; each profile switches on different modules, so the State keeps the choice.
Notes: SPEAKER NOTES Four problems: ownership is fragmented across departments, each with its own system and retention of 7 to 15+ days; nobody can watch or even move 80,000 feeds, which is about 160 Gbps at 2 Mbps; incidents cross borders so evidence is scattered and expires; and department systems must not be disturbed. Our answer is one platform with three deployment profiles from the three briefs: direct unified viewing, federation middleware, and central VMS with regional edge. Shared connectors, events, analyzers and rules mean the State keeps the choice. If asked: Are the three profiles alternatives? The briefs do not say. We built one codebase so the answer does not block us. SOURCES AND DETAIL Problem understanding. The State has tens of thousands of cameras, but each department runs its own standalone system, with its own retention (7 days for some, 15 or more for others) and its own storage, cloud or local. Nobody can watch 80,000 feeds, and nobody can haul them to one place: at 2 Mbps that is 160 Gbps. Incidents cross department and district borders, so evidence is scattered and expires. And departments must be left unaffected. The model: one platform, three deployment profiles, taken from the three requirement briefs (docs/federation-plan.md). Connectors, events, analyzers, rules and search are shared; each profile switches on different modules, so the State keeps the choice.

## Slide 3: Key features: from camera to alert to evidence
SOLUTION · KEY FEATURES
Onboarding and registry
ONVIF discovery, Hikvision and Dahua channels, RTSP and HLS; each camera probed first.
BUILT
Live wall
WebRTC and HLS from a media server that pulls each camera once for every viewer.
BUILT
AI scene analysis
People, vehicles, brands and unusual activity; model provider is a setting, not code.
BUILT
ANPR and watchlists
Dedicated plate detector and OCR, Indian plate format checks, watchlist and wanted-vehicle hits.
BUILT
Vehicle tracking
Search a plate, rebuild its route on a map, flag impossible legs, export CSV.
BUILT
Events, rules, alerts
Search and tag events; rules by type, camera, department and schedule; signed webhooks.
BUILT
Recording and evidence
Hot, warm and cold tiers, clips without re-encoding, hashed exports with a legal hold.
BUILT · API
Departments and roles
Viewer, operator and admin roles, department scoping of cameras and events, access log.
BUILT
Notes: SPEAKER NOTES Walk left to right, top to bottom, in the order a camera meets them: onboarded and probed, watched on a wall, analysed by a pluggable AI model, plates read by a dedicated service, vehicles tracked across cameras, events turned into rules and alerts, footage recorded with evidence handling, and everything controlled by roles and departments. All eight are built in the repository. If asked: Recording shows built-via-API: there is no timeline or export screen yet. Say so if asked. SOURCES AND DETAIL Walk the features in the order a camera meets them: it is onboarded, watched, analysed, turned into events and alerts, searched and tracked, recorded, and controlled by roles. Every card is built in the repository; the chips say how far each was verified. The live wall uses a media server so the app server does not carry video; analysis calls a pluggable AI provider (Gemini by default, Claude or any OpenAI-compatible endpoint by configuration); plates are read by a dedicated detector and OCR service with a labelled fallback.

## Slide 4: High-level design: five stages from source to screen
SOLUTION · ARCHITECTURE
SOURCES
Cameras: RTSP, ONVIF
Recorders: Hikvision, Dahua
Department video systems
Grid and integrator feeds
INGEST
Source adapters and probe
Media server: WebRTC, HLS
Regional gateways at the edge
Recorder: hot, warm, cold
ANALYSIS
Frame gate
Scene model, pluggable
ANPR service on GPU
Local detector and tamper
EVENTS
Event bus
Event store: Postgres
Rules and alert engine
Webhook and log channels
EXPERIENCE
Live wall and map
Events, alerts, rules
Vehicle tracking, routes
Analytics, exports, API
APPLIES TO EVERY STAGE
Identity and roles
Department scoping
Access log and evidence hashes
Health, heartbeats, platform alerts
Plug-in points. Source adapter, VMS connector, analyzer, event bus, alert channel, cold-tier store: each is an interface with a test suite.
Notes: SPEAKER NOTES Five stages. Sources are cameras, recorders and department systems. Ingest probes each source and relays and records video. Analysis runs a cheap frame gate, then analyzers side by side. Every result becomes an event on a bus, is stored, matched to rules and raised as an alert. The screens and API sit on top. Identity, department scoping, audit and health apply to every stage. The bottom strip is the extensibility story: six interfaces, each with a test suite. If asked: Where does video travel? Not through the app server: the media server pulls each camera once and serves viewers. At scale, analysis and recording sit at the edge. SOURCES AND DETAIL Left to right. Sources are cameras, recorders and department systems. Ingest adapts each source to a common stream and profile, relays video, and records. Analysis runs the frame gate and then analyzers side by side. Every result becomes an event on the bus; events are stored, matched against rules and raised as alerts. Experience is the screens and the API. Underneath, identity, departments, audit and health apply to every stage. The six plug-in points at the bottom are the interoperability story: new cameras, vendors, detectors, storage and alert channels plug in without changing the core.

## Slide 5: Interoperability: open standards in, open interfaces out
SOLUTION · INTEROPERABILITY
INTERFACE | STANDARDS AND PROTOCOLS | STATE
Cameras | RTSP, ONVIF (discovery, profiles, event pull-point), HTTP HLS, MJPEG, snapshots | Built, tested on fakes
Recorders | Hikvision ISAPI, Dahua CGI: channels, device details, live event streams | Built, tested on fakes
Department systems | Read-only connector contract; REST with tokens and XML with Basic auth as references | Built, two references
Video out | WebRTC (WHEP), HLS fMP4, MJPEG through a media server | Built
Events out | HMAC-signed webhooks; event bus (in-process, Redis Streams) | Built; Kafka planned
APIs | REST with OpenAPI description; registry API with key; Firebase ID tokens | Built
Storage | S3-compatible object store (Ceph, MinIO, AWS); Postgres or Timescale | Built, tested on fakes
Government registries | VAHAN, SARTHI, eGujCop, AFIS and NAFIS contracts | Mocks and contracts only
Departments stay unaffected
The connector contract has no method that creates, changes or deletes anything
The HTTP layer allows GET and one sign-in POST
Reference systems count every other request: the count stays zero through sync, polling, restart and removal
Give the connector a read-only account
Notes: SPEAKER NOTES In: RTSP and ONVIF cameras, Hikvision and Dahua recorders, read-only connectors for department systems. Out: WebRTC and HLS video, signed webhooks, an OpenAPI-described REST API, S3-compatible storage. The right-hand card matters most to departments: the connector code has no write method, and the test lab counts every non-read request and asserts zero. Be upfront about the right-hand column: device protocols were tested on fakes, and VAHAN, SARTHI, eGujCop and AFIS or NAFIS are mocks and contracts. If asked: Real devices? None was available; the first real device is a PoC task. Legal basis for registries is the State’s to give. SOURCES AND DETAIL Inbound: RTSP and ONVIF for cameras, Hikvision ISAPI and Dahua CGI for recorders, read-only REST or XML connectors for department video systems. Outbound: WebRTC (WHEP) and HLS for video, signed webhooks and an OpenAPI-described REST API for events and registry. Storage is S3-compatible, so Ceph, MinIO or AWS all work. The honest caveat: ONVIF, Hikvision and Dahua were tested against fakes and reference systems because no real device was available; VAHAN, SARTHI, eGujCop and AFIS or NAFIS are mock connectors and contracts only. The right-hand card is the key reassurance for departments: the connector code has no write method, and a counter in the test lab proves zero writes.

## Slide 6: What the platform detects, and the event each detection raises
SOLUTION · VIDEO ANALYTICS
CAPABILITY | HOW | EVENTS RAISED
Plate reading (ANPR) | YOLOv9-t detector and OCR; format check and correction; confidence per read | plate.read
Watchlist and wanted vehicles | Plate matched to a watchlist and to registry records (mock registry today) | plate.watchlist_match, plate.wanted, plate.vehicle_flagged
Vehicle detection and count | Scene model counts vehicles whether or not a plate is readable | vehicle.seen
Person detection, known faces | Scene model counts people; matches enrolled faces | person.seen, person.known, person.unknown
Intrusion, motion, line crossing | Zone and line on a frame fingerprint, or the recorder’s own analytics | vms.intrusion, vms.motion, vms.line_crossing
Objects, brands, unusual activity | Scene model judgement with reasons | scene.unusual, scene.alert
Camera tampering | Blank, dark or washed-out picture from pixel statistics, no model call | camera.blocked, camera.dark, camera.overexposed
Camera health | Three failed runs, then first good run | camera.offline, camera.online
Limit: the no-AI local detector cannot tell a person from a vehicle, and has been tested on synthetic frames only.
Notes: SPEAKER NOTES Each row is a capability, how it works and the event type it raises, so rules do not care which analyzer produced an event. ANPR uses a YOLOv9-t detector and OCR with Indian-format checks and a confidence. People and vehicle counts, objects and unusual activity come from the scene model. Intrusion, motion and line crossing come from the local detector on cameras with AI off, or from a recorder’s own analytics. Tamper and camera health need no model at all. If asked: Accuracy? ANPR accuracy on Indian plates and on the real feeds is not yet measured; that is the first PoC measurement. The local detector cannot tell a person from a vehicle. SOURCES AND DETAIL Each row is one capability, how it is done, and the event type it raises, so a rule written for one event type works whichever analyzer produced it. Plates: a dedicated YOLOv9-t detector and OCR through the ANPR service; plates are format-checked and corrected for common OCR confusions, with a confidence. People, vehicles, objects and unusual activity come from the scene model. Intrusion, motion and line crossing come from the local detector for cameras with AI switched off, or from a recorder own analytics. Honest limits: the local detector cannot tell a person from a vehicle and has never run on real footage; ANPR accuracy on Indian plates and the real feeds is unmeasured; face matching with hosted models may be refused by the provider.

## Slide 7: Every detection is a timestamped, searchable, exportable event
SOLUTION · VIDEO ANALYTICS
EXAMPLE EVENT (ILLUSTRATIVE)
{
"type": "plate.watchlist_match",
"severity": "critical",
"ts": "2026-10-10T14:21:07Z",
"cameraName": "Ring Road 12",
"department": "Traffic",
"location": { "lat": 21.17, "lng": 72.83 },
"confidence": 0.91,
"tags": ["watchlist"],
"data": { "plate": "GJ05AB1234" }
}
The id is deterministic: a retried job stores the event once.
Search and tag
Free text, type, severity, department, time range, tags, paged results.
Alerts
Open, acknowledged, resolved; repeats fold into one alert; schedule and throttle per rule.
Exports
Log export and vehicle route CSV with UTC timestamps, coordinates, leg speed and flags.
Signed webhooks
JSON with an HMAC signature into a control room or SOC; retried on failure.
Evidence clips
Cut without re-encoding, hashed with SHA-256, held against deletion, with a reason on record.
Notes: SPEAKER NOTES Every detection has the same shape: type, severity, UTC frame time, camera, department, location, confidence, tags and data; the example is illustrative. The id is deterministic so retries store once. Outputs: search and tagging, alerts with a lifecycle, log and route CSV exports with UTC timestamps, signed webhooks, and evidence clips with SHA-256 hashes and a hold. If asked: PDF reports? Not built; CSV exports and the events API are. Say it plainly. SOURCES AND DETAIL The left card is the shape of every detection: a type, a severity, a UTC timestamp from the frame, the camera, department and location, a confidence, tags, and type-specific data. The example is illustrative. The id is deterministic, so a retried job stores the event once. On the right are the outputs: search and tag in the Events tab, alert lifecycle, log and route CSV exports, signed webhooks into a control room, and evidence clips with SHA-256 manifests. Tell the audience a PDF report generator is not built; the CSV exports and the events API are.

## Slide 8: 80,000 cameras fit if the video stays at the edge
SCALABILITY · SUMMARY
1 + 8 + 160
Central site (+ DR), regional hubs, edge nodes of about 500 cameras each
DESIGN
4.5 Mbps
of results reach the centre, instead of 160 Gbps of raw video
MODELLED
~50 GPUs
40 × L4 for plates and detectors, 10 × L40S for scene reasoning
MODELLED
17.4 PB raw
15 days at 1 Mbps: 2 days hot, 5 warm, 8 cold, erasure-coded
MODELLED
5 min / 1 h
RPO and RTO for events, alerts and control plane; evidence RPO near zero
TARGET
₹79 cr
CapEx, then ₹24 cr a year; about ₹410 per camera per month over 5 years
MODELLED
How to read the tags. MEASURED: run on the repo’s capacity suite. MODELLED: derived from it plus stated assumptions. PLANNED: designed, not yet built. Assumptions are listed on the last slide.
Notes: SPEAKER NOTES Start the scalability section here. The message: 80,000 cameras fit if video stays at the edge. Six numbers: the 1 plus 8 plus 160 topology, 4.5 Mbps of results versus 160 Gbps of video, about 50 GPUs, 17.4 PB raw for 15 days, RPO 5 minutes and RTO 1 hour as targets, and about 79 crore one-time and 24 crore a year. Remind the audience of the tags. If asked: Which number is firmest? The 0.54 ms per frame and 28 kbps per 500 cameras are measured. Everything else is modelled from them. SOURCES AND DETAIL The central claim: do not haul video to one place. Analyse and record next to the cameras, send results. 500 cameras are 800 Mbps of video but 28 kbps of results (docs/capacity.md, docs/regional-gateway.md). All other numbers follow from that design choice.

## Slide 9: Three tiers: analyse at the edge, decide at the centre
SCALABILITY · REFERENCE DESIGN
Central
State data centre + DR site
x 1 + 1
Control plane: API, scheduler, alert engine
Postgres / Timescale, 3-node HA
Event bus (Redis Streams, Kafka)
Auth, RBAC, audit, dashboards
Regional hub
~10,000 cameras each
x 8
GPU pool: ANPR and detectors
Cold tier: Ceph, S3 API
Bus mirror, DB read replica
Operator video relay
Edge node
~500 cameras each
x 160
gateway: capture, gate, analyzers
MediaMTX: WebRTC / HLS relay
Recorder: hot + warm tiers
Outbox on disk, signed uplink
Cameras and department systems: RTSP, ONVIF, Hikvision, Dahua, grid, VMS connectors
Results, alerts, evidence thumbnails: ~4.5 Mbps total, HMAC-signed, store-and-forward
Frames to GPU pool, results, clips on demand: ~3 Mbps steady per edge
Raw video stays in the district: 160 Gbps in total, never on the backbone
Notes: SPEAKER NOTES Three tiers. Edge nodes of about 500 cameras analyse and record locally and send only results. Eight regional hubs add GPU pools, cold storage and replicas. The centre holds the control plane and database, with a DR site. The arrows carry numbers: results of about 4.5 Mbps in total reach the centre; raw video of 160 Gbps never leaves the district. The edge tier is built today; the hub tier is the design extension. If asked: Why a hub tier? GPUs and cold storage are cheaper to run in a few places than in 160, and it keeps frames on regional networks. SOURCES AND DETAIL This is the Profile 1 shape from docs/federation-plan.md. The edge node is gateway.ts plus MediaMTX, which exist today. The regional hub tier (GPU pool, cold storage, bus mirror) is the design extension; the app does not yet route through hubs. The centre is server.ts with Postgres, Redis/Kafka.

## Slide 10: Compute by tier: central, regional and edge requirements
01 · COMPUTE
Central
1 primary site + 1 DR site
API / UI: 6 × 16 vCPU, 64 GB, stateless behind a load balancer
Scheduler 1 + standby; 8 workers for any camera without an edge node
Postgres / Timescale: 3 nodes, 64 vCPU, 512 GB, 40 TB NVMe
Bus: 5 Redis / Kafka brokers; 4 observability nodes
Regional hub
8 hubs · ~10,000 cameras each
6 servers, 32 vCPU, 128 GB: bus mirror, DB replica, S3 gateway, video relay
2 GPU hosts with 2 to 3 × L4 each
Ceph cold-tier nodes: ~0.86 PB logical per hub
25 GbE inside the hub, 1 Gbps uplink to the centre
Edge node
160 nodes + 16 spares
16 vCPU, 64 GB, 10 GbE; runs gateway, MediaMTX and the recorder
Writes ~62 MB/s sustained at 1 Mbps per camera (125 MB/s at 2 Mbps)
Disk: 10.8 TB hot and 27 TB warm per node
Needs ~3 modern cores; 16 vCPU leaves headroom for re-encode and peaks
Basis. Platform code costs 0.54 ms per analysed frame, flat from 500 to 80,000 cameras (measured). Hardware is provisioned at about 4× the modelled need because every measurement came from one shared Celeron laptop.
Notes: SPEAKER NOTES Central: stateless API pods, a scheduler with a standby, workers, a three-node Postgres or Timescale cluster, a message bus. Hub: six servers plus GPU hosts plus cold-tier nodes. Edge: 16 vCPU and 64 GB per 500 cameras. The edge need is about 3 modern cores; we provision for about four times the modelled need because everything was measured on one weak laptop. If asked: Why 4x headroom? Honest uncertainty. The PoC replaces it with a measured figure and the number can shrink. SOURCES AND DETAIL Edge sizing: 500 cameras need about 2.8 Celeron-cores for capture, gate and platform code at 60 s (docs/capacity.md section 4) plus 3 to 5.5 Celeron-cores of MediaMTX pass-through (about 0.6 to 1.1 percent of a core and 1 MB per camera). That is about 3 modern cores if a server core is 3x a Celeron core (an assumption). 16 vCPU leaves room for H.265 re-encode slots and peaks. Re-encoding capacity itself was not measured. Central: the scheduler measured 48 ms average per tick at 80,000 cameras and about 1.4 GB process memory.

## Slide 11: The platform’s own code is not the limit at 80,000 cameras
01 · COMPUTE
Scheduler tick, average milliseconds, by fleet size
Chart: cameras
| 500 | 5,000 | 20,000 | 80,000
ms per tick | 0.6 | 1.2 | 3.8 | 48
0.54 ms
CPU per analysed frame, flat across the whole range
MEASURED
0 late runs
in 150,194 analyses at 80,000 cameras
MEASURED
1.4 GB
process memory at 80,000 cameras; budget 2 GB
MEASURED
0.125 s
CPU per RTSP still grab; start-up dominates, the largest saving available
MEASURED
Limit of the evidence. One shared Celeron N4020 laptop, with Gemini and the camera frame faked. The on-site PoC re-runs this on target servers.
Notes: SPEAKER NOTES This is the measured part. Our real analysis code, analyzers and alert engine ran at 500, 5,000, 20,000 and 80,000 simulated cameras. CPU per analysed frame was flat at 0.54 ms. At 80,000 cameras the scheduler tick averaged 48 ms, no run was late, memory reached 1.4 GB. The biggest cost we control is starting an ffmpeg process per frame, which is why it is the first optimisation. If asked: What was faked? The camera frame and the model answer. So this measures our code, not capture, not the model, not the database. SOURCES AND DETAIL Source: scripts/capacity/controlPlane.ts running the real analysis worker, analyzer pipeline, event derivation and alert engine, with the camera frame and the model answer faked. Hardware: Celeron N4020, 2 cores at 1.1 GHz, shared with a browser. Capture cost: ffmpeg start-up dominates (0.125 s CPU per still grab versus 0.016 s of ffmpeg accounting).

## Slide 12: About 50 GPUs cover plates, detectors and scene reasoning
02 · ACCELERATORS
A Plate reading (ANPR)
YOLOv9-t detector + CCT-s OCR on ONNX CUDA
333 analyses/s × 40% with vehicles = ~130 reads/s
Peak × 3 = ~400 reads/s
Assume 100 reads/s per L4
16 × L4
2 per hub, so one can fail
SERVICE BUILT
B Real-time detectors
Person, vehicle, intrusion on priority cameras
5% of cameras = 4,000 at 2 fps = 8,000 fps
Assume 500 fps per L4 for a small detector
+20% headroom
20 × L4
2 to 3 per hub, 4 cold spares
PLANNED
C Scene reasoning (VLM)
Self-hosted vision-language model, or a hosted API
Funnel leaves ~67 calls/s (see next slide)
Assume 8 requests/s per L40S
+1 spare
10 × L40S
Central, behind one endpoint
ENDPOINT BUILT
Unmeasured. No GPU has run this stack yet. Throughput per card is the first number the PoC measures. A hosted model API removes Pool C (see cost).
Notes: SPEAKER NOTES Three pools. A: plate reading, about 130 reads a second at fleet level, peaked at 400, assuming 100 per L4, giving 16 L4. B: real-time detectors on 5 percent of cameras at 2 fps, assuming 500 fps per L4, giving 20 L4. C: scene reasoning, about 67 calls a second after the funnel, assuming 8 requests a second per L40S, giving 10. A hosted model API removes pool C. Be clear that throughput per card is an assumption. If asked: Why not more? The funnel on the next slide keeps model load small. What if throughput is half? GPU count doubles; the cost sensitivity is small next to storage. SOURCES AND DETAIL Pool A: the ANPR service (anpr-service/) runs a YOLOv9-t plate detector and a CCT-s OCR model through ONNX Runtime, CPU or CUDA; ANPR_DEVICE=cuda refuses to start without a working GPU. Throughput per card is an assumption, not a measurement; scripts/check-anpr.mjs measures it on real hardware and every response carries elapsed_ms. Pool B is new work: a local detector behind the existing analyzer contract. Pool C: AI_PROVIDER=openai with OPENAI_BASE_URL supports a self-hosted vLLM endpoint.

## Slide 13: A three-stage funnel keeps the model load small
02 · ACCELERATORS
1,333 /s
All cameras, one frame per 60 s
Capture at the edge, nothing leaves the region yet
333 /s
Frame gate: scene changed
25% pass (assumed); heartbeat every 10 min
67 /s
Local detector and ANPR flag it
20% of gated frames (assumed) need scene reasoning
33 /s
Notable events with evidence
10% of results; thumbnails go to the centre
Levers that move the GPU count
Interval 60 s to 300 s: five times fewer frames
Gate threshold per camera type
ANPR only on cameras that see vehicles
Hosted model API instead of Pool C
Mode per camera: AI off runs the local detector only, no model call
Fail-safe. If the ANPR service is down, the scene model reads plates and marks them gemini-fallback, so reads are never mistaken for dedicated OCR.
Notes: SPEAKER NOTES From 1,333 captures a second, the frame gate passes about a quarter, the local detector and ANPR flag a fifth of those, and about 33 a second are notable events with evidence. The right panel lists the levers: a 300-second interval is five times fewer frames; AI-off cameras use only the local detector. The 25 percent and 20 percent are assumptions and the most valuable numbers to measure on real scenes. If asked: What if the gate passes more? Model calls and pool C scale with it linearly. SOURCES AND DETAIL Numbers: 80,000 cameras at one frame per 60 s is 1,333 captures per second. The frame gate (server/frameGate.ts, 2 percent pixel change, 10-minute heartbeat) is assumed to pass 25 percent; that pass rate is the most valuable number to measure on real scenes. The local no-AI detector (server/analytics/localDetector.ts) and ANPR act as the second stage; the 20 percent pass is an assumption. Notable share of 10 percent is also an assumption from docs/capacity.md.

## Slide 14: Bandwidth: the backbone carries results, not video
03 · NETWORK
Cameras to edge
160 Gbps
1 Gbps per node at 2 Mbps; stays inside the district network
Edge to hub
3 Mbps
steady per edge: frames for the GPU pool, results, thumbnails. Provision 100 Mbps for live tiles and clip pulls
Hub to centre
20 Mbps
all hubs together: 4.5 Mbps of results + ~16 Mbps thumbnails. Provision 1 Gbps per hub
Centre to DR
9 Mbps
average database replication (~100 GB a day with indexes). Provision 1 Gbps
28,000×
less than hauling video: 500 cameras are 800 Mbps of video but 28 kbps of results
MEASURED
Live viewing is pulled on demand
An operator wall of 16 sub-stream tiles at 0.5 Mbps is ~8 Mbps. 100 walls at once is ~0.8 Gbps, served from the edge nearest each camera. The media server pulls each camera once however many people watch.
Notes: SPEAKER NOTES Follow the hops: 160 Gbps stays inside districts; each edge sends about 3 Mbps steady to its hub; all hubs together send about 20 Mbps to the centre; database replication to DR averages about 9 Mbps. Link provisioning is much larger than steady state to absorb live viewing and clip pulls. The measured headline: 500 cameras are 800 Mbps of video but 28 kbps of results, 28,000 times less. If asked: Live walls? Pulled on demand from the nearest edge: 16 sub-stream tiles is about 8 Mbps per operator. SOURCES AND DETAIL Camera to edge: 500 x 2 Mbps = 1 Gbps per node, 160 Gbps in total (at 1 Mbps, half). Edge to hub: JPEG frames for the GPU pool (about 2.08 analyses/s per 500 cameras x ~150 KB = 2.5 Mbps) plus results (28 kbps, measured) plus evidence thumbnails (about 0.1 Mbps). Hub to centre: 333 analyses/s x ~1.7 KB = 4.5 Mbps results, plus about 16 Mbps of thumbnails. DR replication: ~100 GB/day of rows including indexes (index factor assumed 2) = 9 Mbps average. The 28,000x figure: 800 Mbps of video versus 28 kbps of results for 500 cameras (docs/regional-gateway.md).

## Slide 15: Eight low-bandwidth strategies, most already in the code
03 · NETWORK
Analyse at the edge
Only results cross the link: about 28 kbps for 500 cameras.
BUILT
Frame gate
Skip a frame if under 2% of pixels moved; heartbeat every 10 minutes.
BUILT
Store and forward
Disk outbox, batches of 200, back-off from 1 s to 60 s, survives days offline.
BUILT
Pull only when watched
One pull per camera; the relay serves every viewer from that one stream.
BUILT
Link-aware playback
Plain fMP4 HLS on weak links; low-latency HLS stalled at 300 ms delay in testing.
BUILT
Sub-streams
Walls and recording on 1 Mbps sub-streams instead of 2 to 4 Mbps main streams.
CONFIG
No-AI local detector
Motion, zone and line events from a 64×36 fingerprint: no model call, no key.
BUILT
Longer intervals
300 s intervals cut frames five times; notable-only mirroring cuts writes tenfold.
BUILT
Notes: SPEAKER NOTES Eight strategies and seven are already in the code: analyse at the edge, the frame gate, a disk outbox with back-off, pulling video only when watched, plain HLS on weak links because low-latency HLS stalled at 300 ms delay, no-AI local detection, and longer intervals with notable-only mirroring. Sub-streams are a configuration choice. If asked: What if the link is down for days? The outbox keeps analysing and replays in order; the oldest results are dropped only past a size or age limit and that is reported. SOURCES AND DETAIL Sources: docs/regional-gateway.md (outbox, back-off, batching), docs/scale-out.md (frame gate, notable mode), docs/media-server.md (on-demand pull, HLS fmp4 versus low-latency HLS that stalled at 300 ms delay, H.265 handling), server/analytics/localDetector.ts (no-AI detector), docs/recording.md (sub-stream recording).

## Slide 16: Hot, warm and cold tiers for a 15-day retention baseline
04 · STORAGE
80,000
cameras recorded
1 Mbps
sub-stream, 10.8 GB per day each
864 TB
written per day
15 days
baseline; per-camera keepDays
Hot · day 0 to 2
Warm · day 3 to 7
Cold · day 8 to 15
Hot
Edge node, local RAID-6 disks with NVMe cache
1.73 PB logical, 2.16 PB raw
10.8 TB per edge node
Live tail and instant playback
MODELLED
Warm
Edge node, warm folder, erasure coded 6+2
4.32 PB logical, 5.76 PB raw
27 TB per edge node
Playback and clips, slower first byte
MODELLED
Cold
Regional hub Ceph, S3 API, erasure coded 8+3
6.91 PB logical, 9.50 PB raw
0.86 PB logical per hub
Clips cut from a 2 GB cache after download
MODELLED
Notes: SPEAKER NOTES Assumptions: 80,000 cameras, a 1 Mbps sub-stream, which is 10.8 GB a day each and 864 TB a day. For a 15-day baseline: hot for days 0 to 2 at the edge, warm for days 3 to 7 on edge disks with erasure coding, cold for days 8 to 15 on regional object storage. That is 1.73, 4.32 and 6.91 PB logical; 2.16, 5.76 and 9.50 PB raw; 17.4 PB in total. If asked: Why not central storage? 160 Gbps of ingest. Departments differ, 7 to 15+ days, so retention is a per-camera policy. SOURCES AND DETAIL Bitrate arithmetic: B Mbit/s uses B x 10.8 GB per day per camera. 80,000 cameras at 1 Mbps is 864 TB per day. Hot 2 days = 1.73 PB logical; warm days 3 to 7 = 4.32 PB; cold days 8 to 15 = 6.91 PB. Overheads assumed: RAID-6 1.25x, erasure coding 6+2 = 1.33x, 8+3 = 1.375x, giving 2.16 + 5.76 + 9.50 = 17.4 PB raw. The tier mechanics (hot to warm to cold to delete, holds blocking every step) are built in server/recording; tested with synthetic video and a signature-checking fake S3, not a real Ceph. Departments differ: 7 to 15+ days, some cloud, some local, which is why the baseline is per-camera policy (keepDays).

## Slide 17: Retention and bitrate move storage by about 17 times
04 · STORAGE
Raw storage by tier, petabytes
Chart: 
| 7 d, 1 Mbps: 7.9 PB | 15 d, 1 Mbps: 17.4 PB | 30 d, 1 Mbps: 35.2 PB | 15 d, 2 Mbps: 34.8 PB
Hot | 2.16 | 2.16 | 2.16 | 4.32
Warm | 5.76 | 5.76 | 5.76 | 11.52
Cold | 0 | 9.5 | 27.3 | 19
Events and logs
86 M events a day, ~48 GB of rows (~100 GB with indexes). 30 days hot in Postgres / Timescale, then compressed for a year.
MODELLED
Departments keep video
In the federated profile, departments hold footage for 7 to 15+ days. The platform keeps metadata and says "video no longer held" when it is gone.
PLANNED
Evidence
An exported clip is hashed, gets a hold, and is copied to the DR site, so it outlives routine retention.
HOLD BUILT
Notes: SPEAKER NOTES The same design at 7 days is 7.9 PB raw; at 30 days 35 PB; at 2 Mbps for 15 days 35 PB. Together bitrate and retention move storage about 17 times, so retention is the first decision to put to the State. Side cards: events about 48 GB a day of rows, departments keeping their own video in the federated profile, and evidence copied to DR. If asked: Cheapest lever? Per-camera retention and sub-streams. If departments keep video, the platform stores only metadata. SOURCES AND DETAIL Raw petabytes by tier. 7 days: 2 hot + 5 warm, no cold. 30 days: 23 cold days = 19.87 PB logical x 1.375 = 27.3 PB raw. 2 Mbps doubles every tier. Logical range from docs/federation-plan.md: 6.0 PB (80,000 cameras, 1 Mbps, 7 days) to 103.7 PB (4 Mbps, 30 days). Event store: 86.4 M events per day at 80,000 cameras, 48.4 GB per day of row data (docs/capacity.md); index overhead of 2x is an assumption.

## Slide 18: Load balancing and horizontal scaling: every layer scales out
05 · OPERATIONS
Operators and dashboards
Load balancer: NGINX / Kong or Kubernetes ingress, TLS
API and UI pods × N, stateless
Scheduler (1 + standby) → queue → workers × N
Edge nodes × 160: each runs its own scheduler
Signed ingest /api/gateway/* into the event store
LAYER | HOW IT SCALES | STATUS
API / UI | Add pods; stateless | PLANNED
Analysis workers | Add workers; one job per camera id | BUILT
Scheduler | One is enough: 48 ms per tick at 80,000 | MEASURED
Edge | One node per ~500 cameras, sharded by gatewayId | BUILT
Event store | Batched writes ~900 rows/s per connection; partition by time | MEASURED
Video relay | One pull per camera; ~1% of a core per viewer | MEASURED
GPU pools | Stateless HTTP behind the balancer; /healthz | BUILT
Notes: SPEAKER NOTES Every layer scales out. API pods are stateless behind a load balancer. The scheduler hands jobs through a queue to any number of workers; capacity is workers times concurrency. Edge nodes shard by gateway. One scheduler was enough in the 80,000-camera simulation. Event writes should be batched: about 900 rows a second per connection when batched, about 9 when one at a time. If asked: Has the queue run on real Redis? Not yet; it was exercised with the in-memory backend and fakes. That is on the pilot list. SOURCES AND DETAIL Scheduler/worker split: ANALYSIS_ROLE=scheduler|worker over Redis/BullMQ (server/bullBackend.ts); a job per camera id; capacity = workers x ANALYSIS_CONCURRENCY. Tested only through the in-memory backend and fakes; never run against a real Redis. Kubernetes manifests with autoscaling are gap A23 (not built). Postgres write rate measured on Neon from a laptop: about 900 rows/s with batches of 100, one event at a time about 9 per second; the worker should group several frames per write.

## Slide 19: Monitoring, logging and health checks
05 · OPERATIONS
LAYER | SIGNALS THE PLATFORM ALREADY EMITS
Cameras | camera.offline / camera.online from run history; blocked, dark and over-exposed picture events
Analysis | GET /api/analysis/status: backend, queue depth, skipped-unchanged count, ANPR health and device
Edge nodes | Signed heartbeat; online, degraded or offline after 90 s; gateway.* events feed alert rules
Video relay | Media server log parsed into events; log tail endpoint for operators
GPU service | GET /healthz reports status and cuda or cpu; every reply carries elapsed_ms
Audit | Access log of refusals and sensitive actions, saved in batches to the database
Central stack to add
Prometheus, Alertmanager, Grafana
Central logs: Loki or ELK, structured JSON
OpenTelemetry traces across edge, hub, centre
One synthetic probe per hub
PLANNED
Golden signals per region
Analyses per second and late runs
Outbox depth and heartbeat age
Disk free and recorder gaps
GPU utilisation and reads per second
Notes: SPEAKER NOTES Left: signals the platform already emits, for cameras, analysis, edge heartbeats, the media server, the GPU service and an access log. Right: what to add centrally: Prometheus, Alertmanager and Grafana, central logs, distributed traces, synthetic probes. The golden signals per region: analyses per second, outbox depth, heartbeat age, disk free, GPU utilisation. If asked: Known gap: a low-disk alert is not wired yet; the usage endpoint exists. SOURCES AND DETAIL Existing signals: camera.offline and camera.online derived from run history; camera.blocked, camera.dark, camera.overexposed from the tamper analyzer; GET /api/analysis/status; gateway heartbeat with online, degraded, offline after 90 s and gateway.* events; the MediaMTX log parser (server/mediaEvents.ts); ANPR GET /healthz; the access log (last 2,000 in memory, batched to Firestore, 5,000-entry queue). Known gap: disk-full is not alerted (GET /api/recordings/usage exists, wiring it to an alert is a small follow-up).

## Slide 20: High availability, backup and disaster recovery
06 · RESILIENCE
RPO ≤ 5 min
events, alerts, config
RTO ≤ 1 h
control plane at the DR site
RPO ≈ 0
held evidence (replicated)
COMPONENT | HIGH AVAILABILITY | BACKUP | DISASTER RECOVERY
Event database | 1 primary + 2 replicas, automatic failover | WAL archive to object store; daily base copy | Async replica at DR site
Bus and queue | 3 to 5 brokers, replication 3 | Topic replay window of 7 days | Mirrored to DR
Control plane | ≥3 pods across racks; standby scheduler | Stateless; config in Git | Warm standby, DNS cut-over
Edge node | 1 spare per 10; cameras re-pointed by gatewayId; outbox holds 7 days | Camera list re-fetched from the centre | Keeps analysing offline, replays in order
Video storage | RAID-6 hot; erasure coding 6+2 warm, 8+3 cold | Not backed up (routine footage) | Region loss costs routine footage; evidence survives
DESIGN: A22 / A23 NOT BUILT
Built today: edge outbox with replay, idempotent event ids, evidence holds. Quarterly failover drills are part of the plan.
Notes: SPEAKER NOTES Targets, to be confirmed with the State: events and config recover within 5 minutes of data and 1 hour of time; held evidence is replicated so loss is near zero. Walk the table by component. Routine video is not backed up: losing a region loses routine footage but never held evidence. What is built is the edge outbox, idempotent events and holds; the rest is design. If asked: A dead edge node? Cameras are re-pointed by gateway id to a spare; this is manual today. That is a known gap. SOURCES AND DETAIL RPO and RTO are proposals for the State to confirm, not measurements. What is built: edge outbox and replay (24 gateway tests over real HTTP including a 20,000-item backlog, link cut and restore with nothing lost or doubled), idempotent event ids, evidence holds. Honest gaps: a dead gateway is not taken over by anyone (shown as gateway.offline); the centre keeps its applied-id list in memory so a confirmation lost just before a restart can apply twice; Redis and Kafka were never run; Kubernetes and DR are design only (gaps A22, A23).

## Slide 21: Cybersecurity: what is built, and what the State deployment adds
06 · SECURITY
DOMAIN
BUILT INTO THE PLATFORM
ADDED FOR THE STATE DEPLOYMENT
Identity
Sign-in, role claims (viewer, operator, admin), department scoping, access log of refusals and sensitive actions
SSO and multi-factor, privileged-access workflow, revoked-token checks on
Edge trust
HMAC-SHA256 signed requests with time and nonce; secrets rotate or disable; a stolen secret reaches only its own cameras
mutual TLS, certificate rotation, signed software updates for edge nodes
Data
SHA-256 evidence manifests, holds, camera credentials sealed, keys held server-side only
AES-256 at rest, TLS 1.3 everywhere, KMS or HSM, signed manifests
Network
Edge reaches out; the GPU service is exposed through an outbound tunnel, no inbound port
Camera VLANs, edge DMZ, per-department segments, WAF and rate limits
Operations
Alert rules on gateway and camera health events
SIEM feed, vulnerability scans, penetration test, independent audit, immutable backups
Notes: SPEAKER NOTES Two columns per domain: built, and added for the State deployment. Built: role claims and department scoping, a recorded access log, HMAC-signed edge requests with replay protection and per-gateway secrets, hashed evidence, sealed camera credentials, server-side keys. Added: SSO and MFA, mutual TLS, encryption at rest and in transit, KMS, network segmentation, SIEM, penetration test and independent audit. If asked: Compliance? The audit and alignment with applicable government guidelines are a planned work item, not a claim. SOURCES AND DETAIL Built: Firebase Auth with role custom claims (viewer, operator, admin) and department scoping (docs/authz.md); access log; HMAC-SHA256 gateway signing over method, path, body hash, time and nonce with 5-minute skew and replay refusal (docs/regional-gateway.md); per-gateway secret rotate and disable; SHA-256 evidence manifests and holds (docs/recording.md); API keys server-side only; ANPR shared key. Not built (gap A21): encryption at rest, mTLS, network segmentation, KMS, signed manifests, SIEM export, gateway software updates. Compliance alignment is a plan item, not a claim.

## Slide 22: Implementation cost: about ₹79 crore one-time
07 · COST
One-time cost, ₹ crore
Chart: 
| Engineering, 24 months | Storage, 3 tiers | Edge servers (176) | Camera onboarding | Contingency 10% | Regional hubs (8) | GPUs and hosts | Central site | Edge network | DR site | Security and audit | Training
crore | 18 | 14.9 | 10.6 | 8 | 7.2 | 5.8 | 3.6 | 3.6 | 2.4 | 2.2 | 1.5 | 1
₹78.8 cr
Hardware 43.1, implementation 28.5, contingency 7.2
Unit prices assumed
Raw storage ₹8,000 to 10,000 per TB, complete
Edge server ₹6 lakh
L4 ₹2.8 lakh; L40S ₹9 lakh
Engineer ₹2.5 lakh per month
Onboarding ₹1,000 per camera
MODELLED ±30%
Notes: SPEAKER NOTES About 79 crore one-time: 43 crore of hardware, 28.5 crore of implementation, 7 crore contingency. Storage, engineering and edge servers are the biggest lines. The unit prices on the right are assumptions and the whole is budgetary, plus or minus 30 percent. If asked: Where are quotes? None yet; replace the unit prices with procurement rates and the model follows. SOURCES AND DETAIL Budgetary, +/-30 percent, for the 15-day, 1 Mbps baseline. Unit prices (assumed): storage per raw TB hot 10,000 / warm 8,000 / cold 8,500 rupees including servers, network and 5-year support; edge server 6 lakh; L4 2.8 lakh; L40S 9 lakh. Storage: 2,160 TB x 10k + 5,760 TB x 8k + 9,500 TB x 8.5k = 14.9 crore. Edge: 176 servers x 6 lakh = 10.6 crore + 2.4 crore network. Engineering: 30 people x 24 months x 2.5 lakh = 18 crore. Onboarding: 80,000 cameras x 1,000 rupees = 8 crore. Contingency 10 percent. Hardware 43.1, implementation 28.5, contingency 7.2, total 78.8.

## Slide 23: Operating cost: about ₹24 crore a year, ₹410 per camera per month
07 · COST
Cumulative cost, ₹ crore
Chart: 
| Y0 | Y1 | Y2 | Y3 | Y4 | Y5
cumulative | 78.8 | 99.8 | 124.2 | 148.6 | 173 | 197.4
ANNUAL RUN COST | ₹ CR
Operations team (SOC, SRE, support, 8 developers) | 7.8
Network links (may use the State network) | 6.2
Power and cooling (~450 kW IT load) | 5.0
Hardware support, from year 2 | 3.4
Software support and audits | 2.0
Total, steady state | 24.4
What moves the number
30-day retention: +₹15 cr storage
2 Mbps recording: +₹15 cr
Hosted model API: −₹1.4 cr now, +₹6 cr a year
Notes: SPEAKER NOTES About 24 crore a year at steady state, led by the operations team, network links, and power. Cumulative 5-year cost is about 197 crore, or about 410 rupees per camera per month. Sensitivities: 30-day retention adds about 15 crore; 2 Mbps adds about 15; a hosted model API saves about 1.4 crore up front but costs about 6 crore a year. If asked: Network cost might ride the existing State network, which would lower this. SOURCES AND DETAIL Annual: power 5.0 (about 450 kW IT load x PUE 1.6 x 8,760 h x 8 rupees per kWh), hardware support 3.4 (8 percent of 43.1, from year 2), operations 7.8 (18 + 8 people x 2.5 lakh x 12), network 6.2 (160 x 25,000 per month x 12 + 8 x 1.5 lakh x 12; may ride the existing State network), software support 1.5, audits 0.5 = 24.4. Year 1 has warranty so 21.0. Cumulative: 78.8, 99.8, 124.2, 148.6, 173.0, 197.4 crore. Per camera per month: 197.4 crore / (80,000 x 60) = about 411 rupees. Sensitivities: 30-day retention adds 15.1 crore of storage; 2 Mbps at 15 days adds 14.9; a hosted model API instead of 10 L40S saves about 1.4 crore up front but costs about 6.3 crore a year at an assumed 0.03 rupees per call (5.76 M calls a day), so self-hosting wins at this volume (benchmark with npm run ai:bench).

## Slide 24: What is verified, and what the PoC must still prove
08 · EVIDENCE
Verified so far
Control plane simulated to 80,000 cameras: 150,194 analyses, no late runs
Edge protocol: 24 tests over real HTTP, 20,000-item backlog, link cut and restored, nothing lost or doubled
Cold tier against a signature-checking S3: lost uploads, 40 MB streamed upload, clips with identical hashes
Real media server: pass-through about 1% of a core per camera
Event stores on real Postgres: ~900 rows/s batched, answers match the in-memory store
Not yet verified
Redis queue, Kafka, Ceph, Kubernetes: written against fakes or not written
Any GPU: ANPR speed and accuracy on CUDA, on Indian plates
Real cameras, H.265, links of hundreds of kilometres
Model latency and cost, and the real frame-gate pass rate on real scenes
Regional hub tier, edge clip fetch, gateway failover, encryption at rest, DR drills
Notes: SPEAKER NOTES Say plainly what is proven and what is not. Proven: the control plane simulated to 80,000 cameras; the edge protocol over real HTTP including a 20,000-item backlog; the cold tier against a signature-checking S3; real media-server cost; stores on real Postgres. Not proven: real Redis, Kafka, Ceph, Kubernetes; any GPU; real cameras and WANs; real model latency and gate pass rate; and the hub tier, failover, encryption at rest and DR drills. If asked: This slide is the answer to any “is this tested?” question. SOURCES AND DETAIL This slide exists so the scalability claims are not read as more than they are. Sources: docs/capacity.md section 6 (not measured), docs/regional-gateway.md (not built or verified), docs/recording.md, docs/federation-plan.md gap stack.

## Slide 25: From on-site PoC to 80,000 cameras in three gated phases
08 · POC AND ROLLOUT
PoC
3 months · 100 to 500 cameras
1 edge node, 1 GPU
Own feed + Government feed
ANPR, intrusion, objects, reports
Gate: measured reads/s and gate pass rate
Pilot
6 months · 10,000 cameras
1 regional hub, 10 to 20 edge nodes
Real Redis, Kafka, Ceph
Failover and DR drill
Gate: SLOs met, cost per camera confirmed
Rollout
12 months · 80,000 cameras
8 hubs in waves
DR site live, audit passed
Hand-over to operations
Gate: sign-off per wave
WHAT THE POC MEASURES
01
Frame-gate pass rate on real scenes
02
ANPR reads/s and accuracy per L4
03
Cameras per core with in-process capture
04
Real bitrate per camera and link
05
Kill an edge node, the database primary, a link
Notes: SPEAKER NOTES Three gated phases. PoC for 3 months with 100 to 500 cameras on one edge node and one GPU. Pilot for 6 months with 10,000 cameras and one hub, with real Redis, Kafka and Ceph and a failover drill. Rollout for 12 months in waves. Each gate is a measurement, so the cost and GPU numbers are corrected by data before the next tranche. The five boxes are what the PoC measures. If asked: Phase sizes are proposals for the State to adjust. SOURCES AND DETAIL Phase sizes are proposals. Each gate is a measurement, so the cost and GPU figures in this deck are corrected by data before the next tranche is committed. The PoC runs on the participant feed and the Government-provided feed.

## Slide 26: Assumption register: change one, and the numbers follow
APPENDIX · ASSUMPTIONS
# | ASSUMPTION | VALUE | SOURCE | IF WRONG
1 | Fleet and sampling | 80,000 cameras, 1 frame per 60 s | Brief; capacity model | Scales captures linearly
2 | Frame-gate pass rate | 25% | Assumed | Model calls and GPUs scale with it
3 | Second-stage pass rate | 20% of gated frames | Assumed | Pool C size
4 | Server core versus Celeron N4020 core | 3× | Assumed | Edge and central CPU
5 | Vehicle share of analysed frames | 40% | Assumed | Pool A size
6 | GPU throughput | 100 reads/s and 500 fps per L4; 8 req/s per L40S | Assumed | GPU count; measured in PoC
7 | Recorded bitrate and retention | 1 Mbps, 15 days, hot 2 / warm 5 | Planning default | Storage, up to ~17×
8 | Storage overhead | RAID-6 1.25×, EC 6+2 1.33×, EC 8+3 1.375× | Typical | Raw petabytes
9 | Event index overhead | 2× row data | Assumed | Database size
10 | Prices and staffing | See cost slides | Budgetary | ±30% on cost
Notes: SPEAKER NOTES Leave this up during questions. Ten assumptions behind every modelled number, with what happens if each is wrong. Offer to re-run the model with the State’s actual values. If asked: The sizing formulas are in scripts/capacity/model.ts and the tables regenerate from scripts/capacity/report.ts. SOURCES AND DETAIL These are the inputs behind every MODELLED tag. The sizing formulas live in scripts/capacity/model.ts and the tables are reproduced by scripts/capacity/report.ts.